# Snow Storage

Description

Snow may have to be stored during major winter storms to increase street accessibility. It is possible for pollutants such as sediment, organics, oil, and grease to be concentrated at snow storage locations and to impact stormwater quality.

When services are contracted, this written procedure should be provided to the contractor so they have the proper operational procedures. In addition, the contract should specify that the contractor is responsible for abiding by all applicable municipal, state, and federal codes, laws, and regulations.

Procedures

Snow Storage

- Snow should be stored away from storm sewer inlets and waterways.

- When possible, snow should be stored on a pervious surface to allow infiltration.

- Snowmelt runoff should be routed through a best management practice (e.g., stormceptor, extended detention basin, oil/water separator, vegetated buffer) prior to reaching a waterbody.

- Sweep or vacuum impervious snow storage areas once snow has melted.

Employee Training

- Train applicable employees who are involved with snow storage on this written procedure. Information regarding proper storage practices and how to prevent and report spills will be presented during the training.

- Periodically conduct refresher training on the SOP for applicable employees who are involved with snow storage activities.

Records

The following records could be used to document activities performed:

- Records of employee training with sign-in sheet.

References

City of Centennial SOP: Snow Removal SOP, August 2007.

City of Golden SOP: Snow Storage SOP, No Date.

City of Lafayette SOP: Snow Disposal SOP, March 2009.

Optional Additional Resources

Municipal codes and ordinances that relate to snow storage.

Designated snow storage areas.

Include a specific distance (e.g., 100 feet) that the snow storage pile must be away from any inlet or waterway.

# Text boxes

For More Information

Name

Address

City, State

Phone

e-mail

Possible Pollutants

Sediment

Organics

Oil

Grease

Good Housekeeping

Secondary containment

Employee training

Related Procedures

Heavy Equipment and Vehicle Maintenance

Material Storage

Salt and Sand Storage

Snow and Ice Control

Spill Prevention and Response

Street Sweeping

Vehicle Fueling